## Slide 1: Transitioning to IEEE Standard
Streaming Telemetry Transport Protocol
P2664

## Slide 2: IEEE Updates
Publish / Subscribe Model
Publisher Data Access Control
IP Level Security
Configurable Connection Origin
P2664
Atomic Measurement Packets
Reduced Data Loss
Lossless Compression
Scalability (to hardware limits)

## Slide 3: Changes Coming in the IEEE Standard
Added higher time precision options
Some commands simplified / key words changed / unused options dropped
Define Operational Modes now requires a publisher success response to accept proposed subscriber options. Options now include:
  Custom compression algorithms selection for data packet, buffer block, signal index cache and metadata
  Custom UDP cipher encryption algorithm selection
New commands:
  Get Primary Metadata Schema
  Get Signal Selection Metadata Schema
  Confirm Update Cipher Keys
Suggested Metadata for synchrophasors has been improved / standardized.
Includes a recommended Publisher and Subscriber API

## Slide 4: API Status
 | Subscriber | TSCC | Filter Expressions | Reverse Subscriber | Publisher | Reverse Publisher | TLS
GSF |  |  |  |  |  |  | 
C++ |  |  |  |  |  |  | 
C# / C++ |  |  |  | SWIG Update Needed | SWIG Update Needed | SWIG Update Needed | 
Go |  |  |  |  |  |  | 
Python |  |  |  |  |  |  | 
C# Native | In progress |  |  |  |  |  | 
Rust | In progress |  |  |  |  |  | 
Java | In progress |  |  |  |  |  | 
V | In progress |  |  |  |  |  |